## Slide 1: RESEARCH PRESENTATION By Muhammad Imran

## Slide 2
Climate change impact on storm water runoff quantity and quality for changing climate and urbanization
RESEARCH TOPIC

## Slide 3
With future growth in population and climatic trends, how this will impact urban storm runoff?
PROBLEM STATEMENT

## Slide 4: LITERATURE REVIEW
    The impacts of climate change and urbanization on drainage in Helsingborg, Sweden: CSO System
  Two climate scenarios (B2/A2)
  Delta change method for GCM to RCM conversion
  Baseline scenario (19610 – 1990) and future scenario (2071 – 2100) with 6 hours temporal resolution
  Three urbanization trends (current situation with population increase, disconnection of storm water and water demand reduction)
  Increase in population will increase overflow volumes and nutrient load
  Use of SUDS and storm disconnection will reduce the overflow volume and nutrient loading
Notes: Future precipitation simulation resulted in increase in rainfall volume due to increase in frequency not the intensities

## Slide 5: LITERATURE REVIEW
    Analysis of climate change effects on urban runoff – M. Jung 2015
  Study area 85% impervious
  Landuse (residential, commercial, institutional, public areas and school)
  Linear regression analysis was used to extrapolate collected data for future climate scenarios
  Runoff simulation done for 10 year and 100 year return period, rainfall duration (10min, 1 hour), base year 1975 and forecast years of 2020-50
  Flow routing done using dynamic wave method and SCS curve method was used for infiltration
  Modelled peak discharge and runoff volume for all durations and return period increases
Notes: Future scenarios have higher runoff values than baseline model
Short duration scenario have greatest increase in peak discharge and runoff volume

## Slide 6: LITERATURE REVIEW
    Assessment of LID for managing storm water with changing climate
  Study area 85% impervious
  Landuse (residential, commercial, institutional, public areas and school)
  Linear regression analysis was used to extrapolate collected data for future climate scenarios
  Runoff simulation done for 10 year and 100 year return period, rainfall duration (10min, 1 hour), base year 1975 and forecast years of 2020-50
  Flow routing done using dynamic wave method and SCS curve method was used for infiltration
  Modelled peak discharge and runoff volume for all durations and return period increases
Notes: Future scenarios have higher runoff values than baseline model
Short duration scenario have greatest increase in peak discharge and runoff volume

## Slide 7: LITERATURE REVIEW
    Assessment of LID for managing storm water with changing climate
  Study area 85% impervious
  Landuse (residential, commercial, institutional, public areas and school)
  Linear regression analysis was used to extrapolate collected data for future climate scenarios
  Runoff simulation done for 10 year and 100 year return period, rainfall duration (10min, 1 hour), base year 1975 and forecast years of 2020-50
  Flow routing done using dynamic wave method and SCS curve method was used for infiltration
  Modelled peak discharge and runoff volume for all durations and return period increases

## Slide 8: STUDY AREA
    Study area is located in Salt Lake and Utah county
    Study the storm runoff into Utah Lake and Jordan River
    For SWMM model development those watersheds were selected which had higher urban population

## Slide 9: METHODOLOGY
  Two modeling scenarios (Present and Future)
  Land use development
  Climatic trends
  Watershed delineation
  SWMM input parameters estimation
  Precipitation data collection
  Storm water pollutant loading
  Model calibration
Notes: Design storm and continuous modeling

## Slide 10: METHODOLOGY
  Sub-catchment delineation based on following land use types;
        Residential (Single/Multi-Family)
        Commercial and Instituitional
        Green barren and open green
        Water
  SWMM input parameters
        Percent impervious
        Roughness
        Depression storage
        Infiltration - Curve number

## Slide 11: METHODOLOGY
  Parameters estimation
        Land use
        Land cover
        Soil type
        Approach – Area weighted average
  Climate Data

## Slide 12: THANKS!